## Slide 1: ETHANOL: BEYOND for sustainability of sugar industry
Dr. Khandagave, R.B.
Director, S. Nijalingappa Sugar Institute, Belagavi.
1st April, 2023

## Slide 2: Introduction:
Sugarcane is grown in tropical and sub-tropical regions of the world. India is the highest sugarcane producer, followed by the Brazil.
Sugarcane is primarily used for production of sugar and ethanol. The latter is mostly used to produce alcoholic beverages as well as low carbon bio-fuel.
Broadly un-exploited areas are 1. Sugarcane trash that generally remain on the fields after cane harvest, 2) Ash derived from bagasse combustion in cogeneration plants, 3) Press mud cake (PMC) from clarification of the sugarcane juice 4) Vinasse which is the liquid residue after distillation of ethanol and 5)Biogenic CO2 emitted during bagasse combustion and ethanol fermentation.
Assured cane price coupled with favourable climatic conditions the sugarcane in the country is gradually increasing.
The excess production of sugar in the country for the past 4-5 years resulted in increasing the stock of sugar thereby affecting the sugar prices.
The Government of India is implementing the Ethanol Blending Programme (EPB) wherein the surplus sugar can be diverted to production of ethanol.

## Slide 3
India has announced various incentives and remunerative prices for ethanol and fixed the target of achieving 20% blending of ethanol with petrol by 2025.
However, it is most important to plan and move forward the sugar sector without confining to only ethanol, sugar and cogeneration as sugar industry generate plenty of bio-mass / wastes.
In Brazil owing to local policies for promoting the production and use of bio fuels industrial facilities are created both for sugar and bio-ethanol production commonly referred as annexed sugar mills. On the contrary the distillery that only produce bio ethanol has autonomous mills are not common.
In other sugarcane growing countries stand alone sugar mills are also noticed. Globally except some few features the sugar mills have common operational features. In case of annexed sugar mills the yields of residues are different and vary according to the technology and ratio of the end products.

## Slide 5
A bio refinery is simply defined as refinery that converts bio mass / waste to energy and other beneficial products (chemicals). It is the sustainable processing of bio mass into a spectrum of bio based products (food, feed, chemicals, materials) and bio energy (bio fuels, power and / heat).
It also encompasses economy powered by nature or in harmony with nature. The bio-circular economy provides a path of achieving sustainability keeping well being in harmony with nature despite increasing the bio-economy and profitability of the system.

## Slide 7: I. Use of organic residues for Carboxylates, Bio plastics and Bio-fertiliser production.
  Carboxylate platform: Residue from sugarcane industry with high water content viz., press mud cake or vinasse are predestined for bio-technological process with the help of microbes. The production of carboxylates undergo anaerobic fermentation by microbiota which can be used directly in chemical industry or be converted to secondary products or biological process i.e. for production of bio-plastics, fuel, food and feed additives, pharmaceuticals or cosmetics. Now a days different companies are developing bio-processes aiming at carboxylate production for future commercialisation.
  Bio-plastics and bio-polymers: Lactate production is so far not an integral part of any sugarcane bio-refinery but it is considered as an electron donor for the chain elongation and as a preservative agent of bio mass. Cellulose nanofibrils (CNFs) are promising high strength polymerics fabrics derived from the renewable resources with promising characteristics viz., low cost, significant barrier and colloidal properties, bio-degradability, good potential for recycling which make them useful material for the preparation of green electronic products. This can replace or become an alternative source of wood.
  Bio-fertiliser : Composting of press mud cake duly enriched with useful micro flora help in production of bio-compost / fertiliser in augmentation of soil properties. Further the enrichment of nutrient value of bio-compost by adding vinasse from the sugar mills.

## Slide 8: II. Biogas production and utilisation:
The Press mud cake and sugarcane based bagasse are useful for production of biogas through anaerobic digestion. It is estimated that upto 251 M3 of bio mass per tonne of dry sugarcane based bagasse and 480 M3 biogas per tonne of dry press mud cake is obtained.
Despite the anaerobic process digestion it also mitigates water pollution and provide nutrients rich organic manure.
The technology in India is proving viable and many sugar mills are in the process of adopting the technology.
These technologies help in not only enhancing the profitability of the industry but also helps in recycling of many essential nutrients back into the soil.

## Slide 9: III. Bio-fuels:
The sugarcane based bagasse will pose a new challenge for sugar industries due to its decreasing demand in cogeneration plants due to cheaper source of electricity availability.
The bagasse consists of cellulose and hemicelluloses which can mainly contribute in production of bio fuels (biogas, 2G ethanol, butanol, hydrogen and aviation fuel) and bio chemicals (lactic acid, succinic acid, gluconic acid and xylitol).
The press mud cake also has lingocellulose as a major component and other constituents are fine bagasse, wax, protein and also insoluble salts.

## Slide 10: IV. Hydrogen Production:
The declining cost of renewable energy sources like solar photovoltaic (PV) offer new opportunities for the development of hybrid systems integrated within the sugarcane industry.
India receive high solar irradiance is significantly increases the performance of solar project. In case of sugar industry, solar PV systems could be strategically deployed on marginal lands within the sugarcane plantations to produce together with bagasse fuelled cogeneration plants electricity for feeding the grid.
At a times of unfavourable crisis on the spot market the electricity produced should be used for H2 production via water electrolysis.
The flexible carrier, H2 can be used directly as fuel for mobility or in a variety of processes to produce gaseous (CH4 and NH3) and liquid fuels (e.g., Methonol and Di methyl ether), bio based chemical production (e.g., carboxylic acids and alcohols) or even microbial protein production (e.g., yeast).
The ability of using surplus electricity for its operation, it can provide various energy services like grid balance, energy storage and reduction of curtailment of variable renewable energy.
The cost of H2 production will primarily depend on the price of electricity and the capacity factor of electrolyser.
The technological developments are likely to drastically reduce CAPEX and OPEX of H2 production based on water electrolysis.
The anticipated cost reduction for solar PV in the next decades, electro-fuels based on H2 could become competitive with fossil fuels especially in the regions where there is high solar irradiation.

## Slide 11: V. Valorisation of Biogenic CO2 sources:
The sugarcane bio refineries, instead of venting CO2 into the atmosphere, it can be captured either from bagasse combustion, sugarcane juice fermentation or bio gas production from sugarcane residues.
The CO2 thus obtained can be a valuable resource for many industries particularly when it is combined with hydrogen to produce synthetic carbohydrates.

## Slide 12
  a. Fermentation of ethanol production process:
Considering the fermentation results in 0.75 kg of CO2 for each liter of ethanol produced which will help in recovering this by product for subsequent use to reduce emissions while simultaneously generating additional revenue stream for bio refineries.
  b. Combustion of bagasse :
Considerable CO2 capture potential is linked to the combustion stage even if technically more challenging than recovering CO2 from fermentation. Three different types of carbon capture process prevail, viz., pre combustion capture, post combustion capture (PCC) and oxyfuel capture (OFC). For bagasse combustion, PCC and OFC are best suited.
  c. CO2 utilisation:
In future defossilized energy systems, sustainable sources of carbon such as captured from sugarcane bio refineries are likely to play very crucial role both for energetic use (via the production of synthetic hydrocarbons) and material use (e.g., in chemical industry), allowing to reduce GHG (Green House Gases) emissions while increasing the energy yield and or carbon efficiency from the same unit of land .
Sugarcane refineries can also sale the CO2 to food industries for various carbonation process viz., for carbonated soft drinks, water and beer, used in the form of dry ice etc.

## Slide 13: VI. Biogenic Silica from the bagasse ashes:
The sugarcane being a graminaceous culture plant, it accumulates silica in its exterior cell structure .The highest amount of bio silica upto 4006 mg / kg dry weight have been reported for sugarcane bagasse.
After combustion bagasse ashes remain as non volitized mineral fractions including a high fraction of biogenic silica.
The advance application prospects of biogenica silica is multifaceted and finds usage among others as drug delivery carrier, catalyst. Addition in construction material, or industrial applications, concrete, backing material etc.

## Slide 14: VII. Potassic fertiliser:
The industrial waste management and disposal of spent wash, Sugarcane Based bagasse and concentrated spent wash is mainly used as biomass fuels in incineration boiler for steam & power generation in bio refineries.
It is established that the incineration boilers generate substantial amount of ash. The disposal of ash is one of major problem in the industry.
The ash contains higher amount of non-degradable elements such as potash salts. This has high potential as one of the major crop nutrient.
India is a net importer of potassium fertiliser which provides an opportunity for the industry to produce potash fertiliser.

## Slide 15: VIII. R & D approach:
The design and implementation of complex system is very challenging and several downstream technologies (e.g., separation of fermentation products, CO2 capture units) should be improved for a successful deployment of integrated bio refineries in the future.
The techno-economical feasibility assessment of these technologies are to be analysed.
Therefore, to adopt the potential possible products in the circular economy of the sugar industry there has to be a strong R & D activities for screening the new approaches.
The focus should be on improving the efficiency and yield improvement of existing ethanol units by conducting R & D activities in the field of fermentation and distillation.

## Slide 16: The circular economy concept for sugar industry
A simple bio-refinery concept has been already implemented in the sugar industry by extending the product portfolio from sugar only to ethanol, electricity and in some cases including bio-gas.
The present preview further throws light on improve the circular economy approach by fostering a better utilisation of waste and residue streams.

## Slide 18: Conclusions:
The assessment of techno-economic feasibility including the impact on environment required to be done during pre-adoption of newer technology.
The review indicates that, there is a substantial potential in the integrated bio-refineries for improving the circular economy.
By implementing better CO2 utilisation or even sequestration, the circular sugarcane economy might play an important role in defossiling other industry branches that can take advantage of the renewable bio-materials obtained by exploiting the sugarcane wastes and residue to their full extent, thus substituting fossil resources.
However, with the background of suitable R & D output the industry can make a long term decision while implementing innovative ideas. The mitigation of environmental impacts, especially the reduction of GHG emissions should also be taken into account when considering economic feasibility.

## Slide 19
Thank you