## Slide 1: Bitter to sweet journey of Indian sugar mills by ethanol blending petrol programme
SISSTA & SNSI One Day Joint Seminar
1st April 2023,Belgavi
Simanchala Panda
Vasantdada Sugar Institute,Pune

## Slide 2: Indian sugar mills were facing financial crisis
Bitter to sweet journey of Indian sugar mills
Fluctuation of domestic sugar price
Lack of proper policy for sugar export
Increase in FRP/SAP of sugar cane year by year.
EBPP helping hand to
Timely sugar cane payment Farmers
Strengthening the financial capacity of sugar mills
Reduce the export of fossil fuel
Reduction of carbon emission

## Slide 3
Vision Of Govt. Of India on EBPP
Year 2018-19 , Fixation of procurement price of ethanol produced from different feed stocks.
Soft loan to enhance the capacity of existing distillery or for installation of new distillery.
June 2021,Road map for ethanol blending in India 2020-25
Sugar mills are showing interest to divert process feed stocks to produce biofuel.
To achieve E20 target on ESY 2025
Enhance the financial status of Sugar Mills.
Generating Rural employment
Empower rural economic

## Slide 4
Chronological Order of Ethanol Blending in India
The EBP program was lunched for the sale of 5 % ethanol blended petrol in January 2003 .
Blending level of bioethanol at 5% with petrol was made mandatory from October 2008,
The GoI fixed an ad-hoc provisional procurement price of INR 27 per litre for ethanol in the year 2010.
Constitute an expert committee to determine the formula or principle for fixing the price of ethanol in 2010
Gazette Notification was issued, directing OMCs to sell ethanol blended petrol with percentage of ethanol up to 10%,in 2015
12.36% central excise duty levied on ethanol supplied for blending with petrol in April 2015

## Slide 5
Chronological Order of Ethanol Blending in India
The administered price of ethanol was revised to INR 39 per litre (Cabinet Committee on Economic Affairs (CCEA), 2016)
IDR Act Amendment on 14th May 2016 to clarify on the roles of Central and State Government for continuous supply of ethanol.
Allowed conversion of B heavy molasses, sugarcane juice and damaged food grains to ethanol. Fixed differentiated ex-mill ethanol price,ESY 2018-19
Sugar & sugar syrup introduced for ethanol production at fixed remunerative price ,Sept. 2019.
Published “Ethanol Procurement Policy on a long term basis under EBP Programme” & utilize surplus stock of rice lying with (FCI) Oct. 2019
Amendment to National Policy on Biofuels 2018 on June 2022.

## Slide 6
Pricing mechanism of ethanol from sugar sector
Sugar/Sugarcane Juice/Sugar Syrup:
The pricing model is based on Fair and Remunerative Price (FRP) of Sugar Cane on which cost of conversion, depreciation and cost of capital is added to compute the ex-mill price of ethanol.
B Heavy Molasses:
The pricing model followed for B Heavy is linked to the standard cost of sugar on which cost of capital is added to compute the ex-mill price of ethanol.
C HeavyMolasses:
The pricing model followed is based on prices of molasses and ex-mill price of sugar. (refer Niti ayog report 2021 page 29&30).

## Slide 7
Estimated Ethanol Demand To Meet the EBPP(year 2019 -20 to 2025-26)
Ethanol Supply Year | Projected Petrol Sale (Cr. Lts) | Blending (in %) | Requirement of ethanol for blending in Petrol(Cr. litres)
2019-20 | 3413 | 05 | 173
2020-21 | 3908 | 08.5 | 332
2021-22 | 4374 | 10.00 | 437
2022-23 | 4515 | 12.00 | 542
2023-24 | 4656 | 15.00 | 698
2024-25 | 4939 | 20.00 | 988
2025-26 | 5080 | 20.00 | 1016
(Source road-map for ethanol blending in India 2020-25,Ministry of Petroleum and Natural Gas June 2021 page 34)

## Slide 8
Initiatives taken by GOI to meet the E20 target
Notified two interest provision schemes of DFPD :
Interest subsidy at the rate of 6% per annum or 50% of rate of interest charged
Whichever is lower on the loan sanctioned borne by the central government for a period of 5 years.
Exempted, increased in production upto 50%,by change of raw materials
Without any expansion of the existing plant & machinery or technology
Furnishing of “No increase in pollution load certificate” from the concerned State / Union Territory Pollution Control Board

## Slide 9
Initiatives taken by GOI to meet the E20 target
Initiatives
DFPD has developed a web portal to review the progress of upcoming ethanol projects on a real time basis. http://sugarethanol.nic.in
MoEF&CC vide its OM dated 28th January 2021:Relaxed the certificate from MoPNG for the Ethanol Blending Programme.
Concept of Tripartite Agreement between mills/distilleries,
banks and OMCs for help mills/ distilleries to avail loans.
One time registration of ethanol suppliers for long term, ethanol demand for 5 years

## Slide 10
Initiatives taken by GOI to meet the E20 target
Initiatives
OMCs have increased their ethanol storage capacity
Reduction in security deposit and applicable penalty on non-supplied quantity etc(Oct 2020)
GST on Ethanol lowered from 18% to 5%.(June 2018)
Zero waste’ technologies for potash fertilizers from distillery wastes – sustainability with profit

## Slide 11
Achievement by Ethanol blending petrol programme(As on November 2022)
success
story
EBPP
Ethanol blending percentage increased from 1.53% in ESY 2013-14 to 10.% in ESY 2021-22.
Ethanol supply increased from 38 cr. lit. in ESY 2013-14 to 433.6 cr. lit. in ESY 2021-22
Ethanol production capacity increased more than 2.5 times and no. of distilleries increased by 66% in 8 years
The cumulative foreign exchange impact due to EBP programme is estimated over Rs53,894 crores during the period ESY 2014 to 2021-22
OMC's paid sugar mills nearly Rs81,796 Crore towards ethanol supplies, enabling timely payment to farmers.

## Slide 12
Achievement by Ethanol blending petrol programme(As on November 2022)
success
story
EBPP
Multi-modal transportation of ethanol & ethanol blended petrol by Oil Marketing Companies (OMCs).
CO2 emissions lowered by 318.2 lac ton in last 8 years
OMCs have signed Long Term Offtake Agreements (LTOAs) to set up Dedicated Ethanol Plants (DEPs).
Oil Marketing Companies (OMCs) increased their ethanol storage capacity from 5.39 crore litres in November 2017 to 34.4 crore litres till November 2022.

## Slide 13
The concept of Bio-Refinery Model for sugar mills
Bio
Refinery
Model
2G Ethanol plant: Second Generation or 2G ethanol plant can convert agricultural residues like sugar cane bagasse& rice straw
Production of bio-chemicals in the Bio-refinery will improve economics of sugar mills significantly
Bio-CNG can be produced from filter cake can easily replace CNG. This bio-manure produced in the plant is an additional source of revenue.
Some by-products like CO2 is also generated which can generate additional revenue

## Slide 14
Cost–Benefit Analysis of Ethanol by diversion of different feed stocks
Sugar mill can decide the best option for ethanol production
Cost of production exclusively depends:
Sugar cane productivity
Soil and climatic conditions
Sucrose % cane
Regional raw material availability
Availability of skilled man power
Chemical cost
Technology adopted

## Slide 15
Cost–Benefit Analysis of Ethanol by diversion of different feed stocks
Production cost per liter of Bio-ethanol from different feed stocks RS/liter |  |  |  |  | 
Particulars | Mixed Juice route | THK juice route | Syrup route | BH mol. route | CH Mol. route
Feed stock cost | 43.5 | 44 | 47 | 38 | 33
Steam | 4.68 | 4.28 | 3.05 | 3.5 | 3.05
Electricity | 0.4 | 0.4 | 0.4 | 0.4 | 0.4
Chemical | 0.08 | 0.08 | 0.08 | 0.08 | 0.08
Operating cost | 5.65 | 5.65 | 5.00 | 5.00 | 4.65
Manpower | 0.35 | 0.35 | 0.35 | 0.35 | 0.35
Administrative and overhead | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Repair and maintenance | 0.5 | 0.5 | 0.5 | 0.5 | 0.5
Marketing and other expenses | 0.25 | 0.25 | 0.25 | 0.25 | 0.25
Interest | 2.0 | 2.0 | 2.0 | 2.0 | 2.0
Depriciation | 1.65 | 1.65 | 1.65 | 1.65 | 1.65
Total | 59.26 | 59.36 | 60.48 | 51.93 | 46.13

## Slide 16
Cost–Benefit Analysis of Ethanol by diversion of different feed stocks
Production Cost of plantation white sugar & raw sugar per ton of cane
S.No | Particulars | Raw sugar | PWS
1 | Cane price | 3202.00 | 3202.00
2 | Power | 110.00 | 110.00
3 | Chemicals(process+ cleaning +ETP) | 60.00 | 78.00
4 | Salary & wages | 210.00 | 210.00
5 | Packing | 35.00 | 35.00
6 | Repair & maintannance | 125.00 | 125.00
7 | Overhead | 90.00 | 90.00
8 | Depreciation | 50.00 | 50.00
9 | Interest | 100.00 | 100.00
10 | Total production cost(A) | 3982.00 | 4000.00

## Slide 17
Cost–Benefit Analysis of Ethanol by diversion of different feed stocks
Income from sugar & by-products:
Sr.No | Particulars | Rate /kg | Production / ton cane | Price/ton in Rs
1 | Sugar | 33.00 | 105 | 3465.00
2 | Filter cake | 1.00 | 35 | 35.00
3 | Final molasses | 9.00 | 45 | 405.00
4 | Bagasse | 2.00 | 40 | 80.00
5 | Total |  |  | 3985.00
Let Recovery % cane = 10.5% = 105Kg per ton of cane
Sr.No | Particulars | Production cost/Kg | Income/Kg
1 | Plantation White Sugar | Rs37.88 | Rs37.95
2 | Raw Sugar | Rs37.73 | Rs37.95

## Slide 18
Cost Analysis of a 3500 TCD plant Sugar with different capacity distillery
General Information
Sr.No | Particulars | Unit | Quantity
1 | Plant capacity | TCD | 3500
2 | Working days | day | 120
3 | Recovery % cane | % | 10.5
4 | Mixed juice % cane | % | 100
5 | CH molasses % cane | % | 4.00
6 | BH molasses % cane | % | 6.50
7 | Ethanol production/Ton of M.J 150 Brix | Liter | 75
8 | Ethanol prodn/Ton of Thk.J 350 Brix | Liter | 175
9 | Ethanol prodn/Ton of syrup 600 deg Brix | Liter | 300
10 | Ethanol prodn per ton of BH molasses | Liter | 300
11 | Ethanol prodn per ton of CH molasses | Liter | 250

## Slide 19
Cost Analysis of a 3500 TCD plant Sugar with different capacity distillery
Qty. of Feed stocks required for different capacity ethanol plant
Particulars | 35KLPD | 50KLPD | 75KLPD | 100KLPD
Mixed juice in ton | 466.67 | 666.67 | 1000.00 | 1333.33
Thick Juice in ton | 200.00 | 285.72 | 428.57 | 571.43
Syup in ton | 116.67 | 166.67 | 250.00 | 333.33
BH mol. in ton | 118.64 | 169.49 | 254.24 | 338.98
CH mol. in ton | 140.00 | 200.00 | 300.00 | 400.00
Ethanol price per liter from different feed stocks ESY2022-23: From Cane juice/thick juice/Sugar syrup =Rs 65.61
From BH molasses =Rs 60.73 From CH molasses =Rs 49.41

## Slide 20
Cost Analysis of a 3500 TCD plant Sugar with different capacity distillery
Sugar cane diverted to different capacity distillery & boiling house of a 3500 TCD plant with BH & CH molasses production
Sr.N | Particulars | No distillery | 35 KLPD | 50KLPD | 75 KLPD | 100KLPD
1 | Sugar cane to distillery | Nil | 466.67 | 666.67 | 1000 | 1333.33
2 | Sugar cane after diversion | 3500.00 | 3033.33 | 2833.33 | 2500.00 | 2166.67
3 | % sugar cane to boiling house | 100.00 | 86.67 | 80.95 | 71.43 | 61.90
4 | BH mol. production | 227.50 | 197.17 | 184.17 | 162.50 | 140.83
5 | CH mol. production | 140.00 | 121.33 | 113.33 | 100.00 | 86.67
6 | Sugar Production | 367.50 | 318.50 | 297.50 | 262.50 | 227.50

## Slide 21
Cost Analysis of a 3500 TCD plant Sugar with different capacity distillery
A.Feed stock for ethanol:- Mixed Juice
Particulars | PWS | PWS+ 35KLPD | PWS+ 50KLPD | PWS+ 75KLPD | PWS+ 100KLPD
Qty.Ethanol production in lt | Nil | 35000 | 50000 | 75000 | 100000
Qty. Sugar Prodn | 367.50 | 318.50 | 297.50 | 262.50 | 227.50
Cost of ethanol | 0 | 2086700 | 2981000 | 4471500 | 5962000
Cost of Sugar | 13920900 | 12064780 | 11269300 | 9943500 | 8617700
Total cost | 13920900 | 14151480 | 14250300 | 14415000 | 14579700
Income from ethanol | 0 | 2296350 | 3280500 | 4920750 | 6561000
Income from sugar | 13946625 | 12087075 | 11290125 | 9961875 | 8633625
Total income | 13946625 | 14383425 | 14570625 | 14882625 | 15194625
Net profit | 25725.00 | 231945 | 320325 | 467625 | 614925

## Slide 22
Cost Analysis of a 3500 TCD plant Sugar with different capacity distillery
B.Feed stock for ethanol:- Thick Juice
Particulars | Plantation white sugar | PWS+ 35KLPD | PWS+ 50KLPD | PWS+ 75KLPD | PWS+ 100KLPD
Qty.Ethanol production in lt | 0 | 35000 | 50000 | 75000 | 100000
Qty. Sugar Production | 367.5 | 318.5 | 297.5 | 262.5 | 227.5
Cost of ethanol | 0 | 2077600 | 2968000 | 4452000 | 5936000
Cost of Sugar | 13920900 | 12064780 | 11269300 | 9943500 | 8617700
Total cost | 13920900 | 14142380 | 14237300 | 14395500 | 14553700
Income from ethanol | 0 | 2296350 | 3280500 | 4920750 | 6561000
Income from sugar | 13946625 | 12087075 | 11290125 | 9961875 | 8633625
Total income | 13946625 | 14383425 | 14570625 | 14882625 | 15194625
Net profit | 25725 | 241045 | 333325 | 487125 | 640925

## Slide 23
Cost Analysis of a 3500 TCD plant Sugar with different capacity distillery
C.Feed stock for ethanol:- Syrup
Particulars | Plantation white sugar | PWS+ 35KLPD | PWS+ 50KLPD | PWS+ 75KLPD | PWS+ 100KLPD
Qty.Ethanol production in lt | 0 | 35000 | 50000 | 75000 | 100000
Qty. Sugar Production | 367.5 | 318.5 | 297.5 | 262.5 | 227.5
Cost of ethanol | 0 | 2116800 | 3024000 | 4536000 | 6048000
Cost of Sugar | 13920900 | 12064780 | 11269300 | 9943500 | 8617700
Total cost | 13920900 | 14181580 | 14293300 | 14479500 | 14665700
Income from ethanol | 0 | 2296350 | 3280500 | 4920750 | 6561000
Income from sugar | 13946625 | 12087075 | 11290125 | 9961875 | 8633625
Total income | 13946625 | 14383425 | 14570625 | 14882625 | 15194625
Net profit | 25725 | 201845 | 277325 | 403125 | 528925

## Slide 24
Cost Analysis of a 3500 TCD plant Sugar with different capacity distillery
D.Feed stock for ethanol:- BH molasses
When BH molasses diverted for Ethanol production.
Sugar recovery % cane sacrificed due to BH diversion is in the range of 1.30 to 1.50 depends upon the sugar house process.
Consider the average sugar % on cane sacrificed 1.40 %.
So net recovery % cane shall be 10.50-1.4 = 9.1
Secondly the quantity of BH molasses produced is suitable for 65KLPD distillery.
So in this case author is not considering for 75 KLPD & 100KLPD capacity for calculation.

## Slide 25
Cost Analysis of a 3500 TCD plant Sugar with different capacity distillery
D.Feed stock for ethanol:- BH molasses
Particulars | PWS | PWS+ 35KLPD | PWS+50KLPD | PWS+65KLPD
Qty.Ethanol production in lt | 0 | 35000 | 50000 | 65000
Qty. Sugar Production | 318.5 | 318.5 | 318.5 | 318.5
Actual sugar production | 367.5 | 367.5 | 367.5 | 367.5
Quantity of BH molasses prod. | 227.5 | 227.5 | 227.5 | 227.5
Qty of BH mol. to distillery | 0 | 116.667 | 166.667 | 216.667
Balance BH Mol. | 227.5 | 110.833 | 60.833 | 10.833
Cost of ethanol | 0 | 1817550 | 2596500 | 3375450
Cost of Sugar | 12064780 | 12064780 | 12064780 | 12064780
Cost of sugar BH Mol after ethanol | 1856120 |  |  | 
Total cost | 13920900 | 13882330 | 14661280 | 15440230
Income from ethanol | 0 | 2125550 | 3036500 | 3947450
Income from sugar | 12087075 | 12087075 | 12087075 | 12087075
Income from BH molasses | 1890000 | 292600 | 160600 | 28600
Total income | 13977075 | 14505225 | 15284175 | 16063125
Net profit | 56175 | 622895 | 622895 | 622895

## Slide 26
Cost Analysis of a 3500 TCD plant Sugar with different capacity distillery
E.Feed stock for ethanol:- BH molasses +sugar syrup
Particulars | NO distillery | PWS+35KLPD | PWS+ 50KLPD | PWS+ 75KLPD | PWS+ 100KLPD
Qty.Ethanol prodn in lt | 0 | 35000 | 50000 | 65000 | 100000
Qty of cane diverted to distillery | 0 | 466.67 | 666.67 | 1000 | 1333.33
Cane for boiling house | 3500 | 3033.33 | 2833.33 | 2500 | 2166.67
Qty of sugar production | 367.5 | 276.03303 | 257.8330 | 227.5 | 197.16697
Qty of BH molasse prodn | 227.5 | 197.16645 | 184.1664 | 162.5 | 140.83355
Cost of ethanol | 0 | 2116800 | 3024000 | 3931200 | 6048000
Cost of Sugar | 13920900 | 10456131.2 | 9766715.2 | 8617700 | 7468684.82
qty of sugar sacrificed | 0 | 42.46662 | 39.66662 | 35 | 30.33338
Cost of sugar secrificed | 0 | 1608635.57 | 1502571.6 | 1325800 | 1149028.43
Total cost | 13920900 | 14181566.7 | 14293286.74 | 13874700 | 14665713.3
Income from ethanol | 0 | 2296350 | 3280500 | 4264650 | 6561000
Income from sugar | 13946625 | 10475453.5 | 9784763.5 | 8633625 | 7482486.51
Income from BH convert to ethanol | 0 | 1983539.99 | 1852756.987 | 1634787.5 | 1416818.01
Total income | 13946625 | 14755343.58 | 14918020.48 | 14533062.5 | 15460304.52
Net profit | 25725 | 573776.7334 | 624733.7334 | 658362.5 | 794591.2665

## Slide 27
Cost Analysis of a 3500 TCD plant Sugar with different capacity distillery
Net profit from different feed stocks route with different capacity distillery
Particulars | Plantation white sugar | PWS+ 35KLPD | PWS+ 50KLPD | PWS+ 75KLPD | PWS+ 100KLPD
Mixed juice route | 25725 | 231945 | 320325 | 467625 | 614925
Thick juice route | 25725 | 241045 | 333325 | 487125 | 640925
Cane syrup route | 25725 | 201845 | 277325 | 403125 | 528925
BH molasses route | 56175 | 622895 | 622895 | 622895* | **
Syrup+ BH molasses route | 25725 | 573776.7 | 624733.7 | 658362.5 | 794591.2665
*The capacity of distillery is considering 65KLPD ** BH molasses from 3500 TCD plant is not sufficient for 100KLPD

## Slide 28
Conclusion:
Capacity utilization more efficiently by diverting excess sugarcane juice, BH molasses or Sugar cane juice in crushing season & BH molasses for off season to produce ethanol .
Stable of sugar price in domestic market, generating sufficient revenues for sugar mills to make payments to farmers.
Profit margins for sugar mills shall be increased by integrating sugar mills with ethanol distilleries as compare to stand alone sugar mill.
The production costs for integrated sugar mills is lower than standalone sugar mill as well as distilleries .
The installation capacity of distillery shall be minimum 50KLPD attached to sugar mill. So the cost of production of sugar as well as ethanol will reduce & profit margin ultimately increase of sugar mill .
Sugar mill will be financial sustain & also supporting the local economic growth.

## Slide 29
Thanks you