## Slide 1: DIVERSION OF SUGAR CANE DERIVATIVES FOR ETHANOL MANUFACTURING : AN OVERVIEW ON THE CHANGE IN THE DYNAMICS OF THE SUGAR PLANT OPERATION
GODAVARI BIO REFINERIES LTD , SAMEERWADI
Dinesh Sharma ,
General Manager –MFG

## Slide 3
PROLOUGE :
Sugar Industry has gone through the ages with continuous improvements in the technical aspects of
manufacturing like better milling practices , energy efficiency through changes in the designing of vacuum
pans to enable usage of low pressure steams , plate heaters and contact heaters to bring down the
approach temperatures , short retention time clarifiers , de-canters , higher evaporation rates with falling
film evaporators , robust bleeding combinations to increase surface evaporation and thereby reducing the
load on condensers , sugar refining processes , specialty sugars , waste heat recovery systems , so on
and so forth.
All these innovations vastly improved the performance of sugar mills and even made them energy efficient
with lowered cost of production. However , sugar production , as a business , started facing a huge challenge
in the form of large sugar inventory , resulting in liquidity crunch .This phenomenon had nothing to do with
the way the industry was performing as a production house , but had a lot to do with external factors like
imbalance in the SUPPLY - DEMAND ratio.
Come the year 2018 , the ETHANOL BLENDING WITH PETROL policy emerged and changed the fortunes of
sugar industry once for ever . It may not only be due to the improved liquidity or profitability , but due to the
more significant aspects like CONTRIBUTION TO THE FIELD OF SUSTAINABLE FUELS , REDUCTION IN CARBON
FOOT PRINT , not to forget the improved ease of sugar mills to pay the farmers.
This paper attempts to highlight the technical impacts on the sugar process balance , which hitherto was
designed based upon a mass balance where all the extracted juice is processed in the boiling house till the
final product ( SUGAR ) and by-product ( C-Molasses ) are obtained .
In the present scenario , intermediate molasses ( B-Heavy ) and partially , sugar syrup are diverted for ethanol
production , which reduces the energy demand in the crystallization stage which alters the load on juice
evaporators , in addition to other implications like idle capacities in pans & centrifugal ,changes in
water balance of the process etc.

## Slide 4
THE BODY : Dwelling into the details …............
1. IMPACT ON THE EVAPORATION OPERATION :
Clarified Sugar cane juice ( Clear Juice ) is concentrated in a set of evaporators , generally designed on
the following considerations ( it varies from plant to plant ; this is a general picture ) -
a. Quantity of water to be evaporated in evaporators to attain desired Brix ( 60 - 68 % )
b. Quantity of bled vapour to Pans and Juice heaters
c. Bleeding of vapour from 2nd and/ Or 3 rd and / Or 4 th and / Or 5 th effects.
d, Total evaporation targeted - 75 - 80 %
This is achieved by bleeding vapour from different sequenced bodies -
20- 23 % on cane for pans with 2 nd or 3 rd vapour
12 - 16 % on cane for juice heaters from 2nd,3rd and 4 th vapour
Juice heating requirements remaining the same , the bleeding for pans come down in case of diversion and
hence the evaporation load on the subsequent bodies in the evaporator set increases .
If bleeding arrangements are not modified to next lower grade vapors , it either causes lower syrup brixes
OR if the subsequent bodies are large enough , it increases the load on condenser and hence energy loss.
Depending upon the quantity of diversion targeted , bleeding arrangements have to be shifted to next effect
to counter- balance the increased evaporation needs.
2. PAN STATION :
In order to keep a check on steam consumption , number of pans have to be restricted pro-rata as per the
extent of diversion , spare pans can be handful in getting the periodical water boiling / cleaning of pans in
operation , which intern will perform better regularly .
In case of refineries , the idle capacities can be utilized by opting for additional re-processing activities along
with cane crushing , which greatly reduces the cost on power , steam and chemicals .

## Slide 5
3.CENTRIFUGALS :
Centrifugals perform well when loaded optimum. It is always better to run only required units with optimum load rather than running with underload , which causes re-circulation of sugar and unwarranted power consumption.
4.Accuracy in arriving at Recovery & Diversion quantities :
Since the factory input is shared with different process streams , accurate measurement of
quantity of diverted material is of paramount importance to arrive at process efficiencies of both streams.
Guidelines specify the use of Mass flow meter OR Load -cell based weighing scales for the accounting of diversion.
However , it is always better to have load-cell based weighing scale , for its consistency of accuracy and ease with which it can be calibrated.

## Slide 6
5.Quality of Feedstock :
Quality is equally important as the variation in Brix can lead to improper estimation and hence frequency of analyzing Brix and purity to be well defined and adhered to.
It is better to carryout analysis for Brix and TDS by both the plants and even better if cross functional teams engage in analysis of same batch of feed in both laboratories by swapping.
This reduces the possible errors occurring due to differing concentrations , freshness and approximations errors in either of the labs and staff.
If a factory diverts syrup during season and stores B-Heavy molasses for using it as a feedstock during later months , a lot of care has to be taken regarding Brix ( preferably 85 + ) and storage temperatures.
A stringent SOP for the re-circulation and cooling of molasses in storage has to be in place and efficacy of such measures to be checked and validated by periodical analysis to monitor TDS levels.
Also , while completing the process , if lower Brix molasses is generated , it should not be sent to storage , it should be made to consume immediately.
In case of syrup , extra care to be taken from the stages of juice extraction and clarification to avoid contamination and inversion , otherwise volatile acids will interfere with the distillery balance.
Good mill sanitation followed by optimization of chemical dosing is the way
along with regular monitoring of Dextran levels in juice .

## Slide 7
6.Water Management :
In case of syrup diversions of more than 30 % of capacity along with B-Heavy molasses , there will be an increase in the saving of excess hot condensate of sugar plant.
It provides an opportunity to utilize this water as a resource by treating that water in a BTP, so that water needs of the complex can be met resulting in reduction of fresh water consumption.

## Slide 8
Godavari 's journey with EBP …............
Godavari Bio Refineries Ltd , Sameerwadi has been one of the pioneers in the Industry to embrace the EBP program since 2018.
We started with BH diversion and in 2019, next year syrup diversion taken up. Constantly upgrading its capacities to make a significant contribution to the EBP program,
now runs a distillery of 600 KLPD and sugar plant of 18000 TCD.

## Slide 9: YEAR-WISE CANE CRUSHING & ETHANOL PRODUCTION DETAILS
Sl. No. | Particulars | UOM | Season 2018-19 | Season 2019-20 | Season 2020-21 | Season 2021-22 | Season 2022-23 as on 23.03.2023
1 | Total days operated | Days | 115 | 113 | 142 | 154 | 122
2 | Total Cane crushed | MT | 1727269 | 1526610 | 2002849 | 2248238 | 2036410
3 | Cane Diversion ( Through Syrup ) | MT | 0.0 | 350176 | 531767 | 599701 | 697965
4 | Cane Diversion ( Through Syrup ) | % | 0.00 | 22.94 | 26.55 | 26.67 | 34.27
5 | Gross Recovery % Cane | % | 11.92 | 11.10 | 11.40 | 11.60 | 11.82
6 | Total Sugar production - Marketable (White + Refined + Raw) | Qtl. | 1810160 | 1279390 | 1486000 | 1836160 | 1387530
7 | Sugar Diversion through BH+SYP | Qtl. | 281545 | 444411 | 806878 | 942569 | 104515
8 | Sugar Diversion through BH+SYP | % | 13.67 | 26.23 | 35.34 | 36.14 | 42.00
9 | Distillery KLPD | KLPD | 200 | 320 | 400 | 400 | 600
10 | Total Ethanol from CH+ BH+SYP | Cr.Lr | 5.89 | 5.67 | 7.76 | 9.06 | 9.53

## Slide 10
Chart: Total Ethanol (In crore litres ) from BH+SYP
| 2018-19 | 2019-20 | 2020-21 | 2021-22 | 2022-23 Expected
Total Ethanol from CH+ BH+SYP Cr.Liter | 5.8874 | 5.6727 | 7.7591 | 9.0584 | 9.5273

## Slide 11
Chart: 
| 2018-19 | 2019-20 | 2020-21 | 2021-22 | 2022-23 Expected
Cane Diversion ( Through Syrup ) MT | 350176.2185 | 531767.4154 | 599700.6659 | 717965.4255

## Slide 12
Chart: 
| 2018-19 | 2019-20 | 2020-21 | 2021-22 | 2022-23 Expected
Cane Diversion ( Through Syrup ) % | 22.9382 | 26.5505 | 26.6743 | 34.27

## Slide 13
Chart: Sugar Diversion through BH+SYP MT
| 2018-19 | 2019-20 | 2020-21 | 2021-22 | 2022-23 Expected
Sugar Diversion through BH+SYP Qtl. | 28154.4914 | 44441.0799 | 80687.805 | 94256.89 | 104515.09

## Slide 14
Chart: Sugar Diversion through BH+SYP %
| 2018-19 | 2019-20 | 2020-21 | 2021-22 | 2022-23 Expected
Sugar Diversion through BH+SYP % | 13.6745 | 26.2261 | 35.339 | 36.1421 | 42

## Slide 15
CONCLUSION :
EBP is a wonderful platform which has the potential of boosting the sugar industry economy and renders with an opportunity to be a part of SUSSTAINABILITY DRIVE.
With proper modifications and necessary investments in the clarification and evaporation stations , enhancement in capacity can be achieved , so that idle capacity of sugar house can be put to better use.
There is steam & power saving in Sugar Plant , however a well conceived integration of the processes can result in more saving,
In the present scenario , Energy savings are to be captured for the complex as a whole and not merely from the sugar plant point of view , which can truly give a proper perspective on the advantages of diversion.

## Slide 16
An Expression of gratitude …......
The Author extends his gratitude to The CMD , Mr.Samirbhai Somaiya , Godavari Bio Refineries ,for being such a visionary
and taking all of us along in this journey of Godavari.
I should mention the whole team of Godavari Bio Refineries ( Sugar , Co-gen and Distillery ), who have done wonderfully well through
this journey and their collective efforts are commendable.
I thank SISTA & SNSI , Belagavi for providing this platform to the stake holders of the Industry to engage in sharing the experiences .

## Slide 17
THANK YOU ….!