## Slide 1
PRESENTATION ON
SPENT WASH TREATMENT TECHNOLOGY
“RAJ ZERO LIQUID DISCHARGE , AN INNOVATIVE SOLUTION TO TREAT THE DISTILLERY EFFLUENT (SPENT WASH)”
PREPARED BY
RAJ PROCESS EQUIPMENTS & SYSTEMS PVT. LTD.

## Slide 3: TYPICAL CHARACTERISTICS OF RAW SPENT WASH
SR. NO | PARAMETER | FED-BATCH PROCESS
1 | Volume L/L alcohol | 8.0-10.0
2 | Colour | Dark Brown
3 | pH | 4.0-4.2
4 | COD (mg/L) | 120000-140000
5 | BOD (mg/L) | 60000-70000
6 | Total Solids (mg/L) | 160000-210000
7 | Total Volatile Solids (mg/L) | 80000-90000
8 | Inorganic dissolved Solids (mg/L) | 60000-90000
9 | Chlorides (mg/L) | 10000-12000
10 | Sulphates (mg/L) | 8000-10000
11 | Total Nitrogen (mg/L) | 2000-2500
12 | Potassium (mg/L) | 20000-22000

## Slide 4
1. This is “Continuous flow stirred tank reactor process called as (CSTR). It is based on the concept of Conversion of organic matter into Biogas.
2. Spent wash have high potential to produce methane gas and it is subjected to anaerobic digestion for methane recovery. Bio-methanation is an attractive primary treatment process which reduces the BOD by 85 – 90% and COD by 60 – 65% and produces Methane Gas.
BIO METHANATION PROCESS

## Slide 5: COMPRESSED BIOGAS (CBG) – FUEL OF THE FUTURE
1. The biogas purified by removing hydrogen sulphide (H2S), carbon dioxide (CO2), water vapor.
2. Purified Biogas content more than 95% Methane.
3. CBG has calorific value and other properties similar to CNG and hence can be utilized as green renewable automotive fuel.

## Slide 6
1. The two stage Multi Effect Evaporation System which is a combination of Integrated & Standalone Evaporator for concentrating the Biomethanted spent wash upto 45% solid by using Vapours from Analyser to Integrated Effect Evaporator and by providing Steam separately for Stand alone evaporators.
2. The Integrated Evaporation System offered by us , uses Analyser Vapour to concentrate Biomethanated Spent Wash and this saves the steam. The technology adopted is of falling film type.
3. Degasifying system provided helps in removing the ammonia from the spent wash and further prevents foaming.
4. Low Pressure Steam is used to concentrate the Spent Wash upto 45% Solid, It will be a combination of Falling Film & Forced Circulation Bodies.
MULTI EFFECT EVAPORATION PROCESS - (MEE)

## Slide 7: OUR patented TECHNOLOGY
SPENT WASH SPRAY DRYER

## Slide 8: Spray Drying System is automated and require very less Manpower. This system consumes moderate power & low fuel. This system does not require cleaning and it operates for 365 days without any stoppage. Maintenance cost is negligible.

## Slide 9: Process description of SPENT WASH DRYER
The Concentrated Biomethanated Spent wash with 30-40% Solid from the Multiple Effect Evaporator is fed into the Spray Dryer by feed Pump. In the Spray Dryer, the liquid is atomized by high speed Atomizer at the top of the Chamber. The Hot Air is generated by using the Biogas Based Direct Fired Hot Air Generator and further diluting it with the Boiler Flue Gas, High efficient Air Distributor is used to feed Hot Air in Spray Chamber. In Spray Chamber atomized feed is mixed with flue gas as the atomized spent wash comes in contact with the Hot Air, immediately the water Evaporates & free flowing dry powder with less than 5% moisture is discharged from bottom of Chamber, The process air carries fine particles which is further arrested in high efficient cyclone. Very fine particles cannot be arrested in cyclone.

## Slide 10: Process description of SPENT WASH DRYER
This fine particle is scrubbed in wet scrubber. Exhaust of Wet scrubber carries particulate matter below 50 ppm which is within permissible limit of Central Pollution Control Board. The free flowing powder which discharged from Spray Chamber and Cyclone Separator is further conveyed by using pneumatic Handling System. The dried product is separated in a high efficiency cyclone separator and discharged through the Rotary Air Lock Valve. The exhaust air is further passed through a Conveying Bag Filter for recovering the fines not separated in Conveying Cyclone Separator and discharged through the Rotary Air Lock Valve. Clean air is then vented to the atmosphere. The dried powder which is discharged from conveying Cyclone Separator and Conveying Bag filter is get collected at the Powder Storage Silo. Spray Drying System is automated and require very less Manpower. This system consumes moderate power & low fuel. This system does not require cleaning and it operates for 365 days without any stoppage. Maintenance cost is negligible.

## Slide 11: Process Flow Diagram OF SPENT WASH DRYER

## Slide 12: ANALYSIS OF BMSW POWDER
SR. NO | PARAMETER | BMSW POWDER
1 | Moisture | 5 -10 %
2 | Colour | Dark Brown
3 | Potassium (Dissolved Potash) | 18 - 20 %
4 | Total Nitrogen | 1 – 1.5 %
5 | Organic Carbon | 32 – 36 %
6 | Phosphorus | 0.9 – 1 mg/ltr
7 | Total Volatile Acid | 55 – 58 mg/ltr
8 | Chlorides | 680 – 700 mg/ltr
9 | Sulfates | 520 – 540 mg/ltr
10 | Sulfates in Ash | 450 – 460 mg/ltr
11 | Calcium | 230 – 240 mg/ltr
12 | Iron | 455 – 465 mg/kg
14 | Calorific Value | 1800 – 2200 cal/g

## Slide 13: GRANULATION PLANT
Dried Spent wash powder at 5% moisture discharged from Spray Dryer is granulated in the Granulation Plant. Depending upon application we decide the recipe and quantity of other ingredients. We mix spent wash powder with other ingredients in blender. After blending we feed this mixture into granulator. After Granulation we do standard packing as per requirements.
This granule is rich in potash. It contains organic carbon and other minerals. This granule can be stored in bags for longer time. It is easy to handle & transport.
This granule is easily soluble in water. This can be used for various crops as Organic Fertilizer, In India this fertilizer is termed as potash derived from Molasses.
There are many big organizations in India who are selling this product under the Brand Name like Kash, PDM, Brown Potash, Organisoil etc.

## Slide 14: PROCESS FLOW OF GRANULATION PLANT

## Slide 15: HIGHLIGHTS OF BMSW POWDER GRANULATION PLANT
BMSW Powder is granulated by using Binders.
Ash, Sludge can be added in a calculated ratio to enhance nutrient in powder and helps in achieving complete ZLD.
The granules are well rounded, remains dust free and also completely free flowing non caked, even after long storage.

## Slide 16: OFFICE MEMORANDUM
MINISTRY OF CHEMICALS & FERTILIZERS DATED: 12TH JULY 2022

## Slide 17: OFFICE MEMORANDUM
OFFICE OF COMMISSIONER OF SUGAR MAHARASHTRA STATE DATED: 14TH JULY 2022

## Slide 18: PROSPECTIVE CUSTOMERS FOR PDM GRANULES

## Slide 19
Sr. No. | Advanced RAJ-ZLD Technology
1. | Operating Cost : 35-40% Lower
2. | Capital Investment : 30-40% Lower
3. | Cleaning Cycle: Regular boiler Frequent cleaning is not required.
4. | Maintenance Cost : Very lower than incineration boiler
5. | Boiler Capacity suitable for distillery complex, Since no any additional Steam generation.
6 | Steam and Power is Balanced as per Process requirement.
7. | Suitable option for Juice Syrup to Ethanol Case.
ADVANCED RAJ-ZLD TECHNOLOGY

## Slide 20: CASE STUDY FOR DISTILLERY
120 KLPD MOLASSES BASED DISTILLERY

## Slide 21
DISTILLATION
BIO-DIGESTER
INTEGRATED & STANDALONE BMSW EVAPORATION
BMSW SPRAY DRYER
POWDER 54 TPD @ 5% MOISTURE
Gas generation: 36000 Nm3/day
@ 5000 Kcal/Kg. – 15 TPD CBG
RSW- 900 TPD @ 12% w/w solid
Bio-Spent Wash 900 TPD @ 6% w/w solid
135 TPD @ 40% w/w solid
Evaporation 765 TPD
81 TPD Evaporation
H. P.
BOILER
TG
Flue Gas & Bagasse 16 TPD @ 2200 Kcal/Kg
BAGASSE 180 Ton/ Day
H.P STEAM
382 TPD @ 45 Kg/Cm2
BIOGAS TO CBG PLANT – 15 TPD
Fermentation Alc. Conc. 12% V/V
264 TPD
118 TPD
BIO- SPENT WASH CASE
382 TPD @3.5 Kg/cm2
TOTAL STEAM REQUIRED | 400 TPD
BOILER CAPACITY REQUIRED | 18 TPH
TOTAL BAGASSE REQUIRED | 180 TPD

## Slide 22
RSW INCINERATION BOILER
ASH
INCINERATION BOILER
RSW- 900 TPD @ 12% w/w solid
196 TPD @ 55 % w/w solid @ 1750 Kcal/Kg
Evaporation 704 TPD
(40% Bagasse + 60% RSW )
Bagasse 130 TPD @ 2200 Kcal/Kg
TG
STANDALONE RSW EVAPORATION
H.P. STEAM
GENERATED
(600 TPD)
To Condenser
L.P. STEAM 600 TPD @ 3.5 Kg/Cm2
EXCESS L.P. STEAM 164 TPD @ 3.5 Kg/Cm2
STEAM 172 TPD
(7166 Kg/Hr.)
STEAM 264 TPD
(11000 Kg/Hr.)
DISTILLATION
TOTAL STEAM REQUIRED | 436 TPD
BOILER CAPACITY REQUIRED | 25 TPH
TOTAL BAGASSE REQUIRED | 130 TPD

## Slide 23
SL | DESCRIPTION | UNIT | BMSW DRYER (OPTION-I) | INCINERATION BOILER (OPTION-II)
1 | Steam of Distillation & MSDH Plant (2.3 Kg/Lit.) | TPD | 264 | 264
2 | Steam of Evaporation Plant | TPD | 118 | 172
3 | Total Steam Required | TPD | 382 | 436
4 | Boiler Capacity (Installed) | TPH | 20 | 25
A. | BAGASSE CONSUMPTION & ECONOMICS |  |  | 
5 | Bagasse Required for Generation of above mentioned balance Steam (Supplementary Fuel) | TPD | 180 | 130
6 | Bagasse Required for Dryer with with Flue Gas | TPD | 16 | -
7 | Total Bagasse Required Approximate | TPD | 196 | 130
8 | Cost of Bagasse (2500 Rs./MT) | Rs./Day | (4,90,000) | (3,25,000)
9 | Revenue from BMSW Granule Fertilizer (8000 Rs./MT) X 67 TPD | Rs./Day | 5,36,000 | 70,000
10 | Processing Cost for Granule with Bag | Rs/Day | (67,000) | -
11 | Revenue from CBG 15 TPD @ 70,000 | Rs/Day | 10,50,000 | -
12 | Processing Cost for CBG @15000 Rs./MT | Rs/Day | (2,25,000) | -
13 | Net Profit | Rs/Day | 8,04,000 | 2,55,000
14 | Savings Per Day | Rs/Day | 10,59,000 | 
15 | Saving Per liter of Alcohol | Rs/Lit of Alcohol | 8.825 | -

## Slide 24
EXECUTED & ON GOING PROJECT LIST
SR NO. | CUSTOMER NAME | YEAR | CAPACITY | STATUS
1 | KHANDOBA DISTILLERIES PVT LTD | 2018 | 120 KLPD | COMMISIONED
2 | JAKARAYA SUGAR LTD. | 2018 | 120 KLPD | COMMISIONED
3 | RAI BAHADUR NARAIN SINGH SUGUR MILLS LTD | 2020 | 90 KLPD | COMMISIONED
4 | ETHANOL COMPANY LTD | 2020 | 90 KLPD | UNDER EXECUTION
5 | A.B. GRAIN SPIRITS PVT.LTD. | 2020 | 90 KLPD | COMMISIONED
6 | RAI BAHADUR NARAIN SINGH SUGUR MILLS LTD | 2021 | 90 KLPD | COMMISIONED (REPEATED ORDER)
7 | KARMAYOGI ANKUSHRAO TOPE SAMARTH S.S.K. LTD. | 2021 | 60 KLPD | UNDER EXECUTION
8 | DWARKADHISH SAKHAR KARKHANA LTD | 2021 | 90 KLPD | COMMISIONED
9 | SATISH SUGAR LTD | 2021 | 60 KLPD | COMMISIONED

## Slide 25
EXECUTED & ON GOING PROJECT LIST
SR NO. | CUSTOMER NAME | YEAR | CAPACITY | STATUS
10 | SHREE NARMADA KHAND UDYOG SAHAKARI | 2021 | 90 KLPD | COMMISIONED
11 | JAKARAYA SUGAR LTD. | 2021 | 120 KLPD | UNDER EXECUTION (REPEATED ORDER)
12 | INDIAN CANE POWER LTD | 2022 | 200 KLPD | UNDER EXECUTION
13 | NKJ BIOFUEL PRIVATE LIMITED | 2022 | 150 KLPD | UNDER EXECUTION
14 | RENA SAHAKARI SAKHAR KARKHAN LTD | 2022 | 30 KLPD | UNDER EXECUTION
15 | VITTHAL CORPORATION LTD. | 2022 | 150 KLPD | UNDER EXECUTION
16 | SHRI GURUDATT SUGARS LTD | 2022 | 150 KLPD | UNDER EXECUTION
17 | SRI BASAVESHWARA SUGARS LTD. | 2022 | 45 KLPD | UNDER EXECUTION
18 | GANESH BENZOPLAST LTD. (SAGAR DISTILLERY) | 2022 | 150 KLPD | UNDER EXECUTION

## Slide 26
EXECUTED & ON GOING PROJECT LIST
SR NO. | CUSTOMER NAME | YEAR | CAPACITY | STATUS
19 | VILAS SAHAKARI SAKHAR KARKHANA LTD. | 2022 | 60 KLPD | UNDER EXECUTION
20 | VENKATESHKRUPA SUGAR MILLS LTD. | 2022 | 180 KLPD | UNDER EXECUTION
21 | MEKALSUTA SUGARS PVT. LTD. | 2022 | 150 KLPD | UNDER EXECUTION
22 | NARMADA SUGARS PVT. LTD. | 2022 | 200 KLPD | UNDER EXECUTION
23 | CHHATRAPATI SHAHU SSK LTD | 2022 | 180 KLPD | UNDER EXECUTION
24 | BARAMATI AGRO LIMITED | 2022 | 150 KLPD | UNDER EXECUTION
25 | NATURAL SUGAR & ALLIED INDUSTRIES LTD. | 2022 | 90 KLPD | UNDER EXECUTION
26 | CHHATRAPATI SAMBHAJI RAJE SAKHAR UDYOG LTD. | 2022 | 60 KLPD | UNDER EXECUTION
27 | PIYUSH SUGAR & POWER PVT. LTD. | 2022 | 60 KLPD | UNDER EXECUTION

## Slide 27
EXECUTED & ON GOING PROJECT LIST
SR NO. | CUSTOMER NAME | YEAR | CAPACITY | STATUS
28 | SADGURU SRI SRI SAKHAR KARKHANA LTD. | 2022 | 150 KLPD | UNDER EXECUTION
29 | DECCAN SUGAR PVT. LTD. | 2022 | 200 KLPD | UNDER EXECUTION
30 | VISHWASRAO NAIK S.S.K. LTD | 2023 | 60 KLPD | UNDER EXECUTION
31 | VISHWARAJ SUGAR INDUSTRIES LIMITED | 2023 | 250 KLPD | UNDER EXECUTION
32 | SHREENATH MHASKOBA SAKHAR KARKHANA LTD. | 2023 | 90 KLPD | UNDER EXECUTION
33 | UDAGIRI SUGAR AND POWER LIMITED | 2023 | 75 KLPD | UNDER EXECUTION
34 | SIDDAPUR DISTILLERIES LIMITED | 2023 | 220 KLPD | UNDER EXECUTION
35 | M. S. PATIL SUGARS LIMITED | 2023 | 120 KLPD | UNDER EXECUTION

## Slide 28: OUR MANUFACTURING FACILITIES
UNIT I:) BHOSARI UNIT (R & D FACILITY)
UNIT II: CHAKAN UNIT
UNIT III: PABAL UNIT
UNIT IV: SHIRVAL UNIT

## Slide 29: THANKS !!!!
RAJ PROCESS EQUIPMENTS & SYSTEMS PVT. LTD.
Jai Ganesh Vision, “B” Wing, 3rd Floor, Akurdi,
Pune - 411 035, India.
www.rajprocesswquipment.com