## Slide 1
BRIEF INTRODUCTION OF S.K.BHOJARAJ :
Very Good morning. Please refer details given in the paper, “Diversion of BH/ Partial syrup to Ethanol manufacture with Comparision of Evaporator capacities in various configurations & comparision of net steam consumption ,when diversion is not therepartI”.
FULL NAME : SURA. K. BHOJARAJ

## Slide 2
Specific method of Research:
Keeping in view of present day trend , to keep sugar production in control , two routes are selected:
BH diversion ( 2 massecuite boiling) to Ethanol production
Partial syrup diversion (also 2 massecuite boiling ) to Ethanol production ,balance syrup goes for pan boiling .
Based on the operating conditions the Evaporator configurations are arrived in each case.
RESEARCH DESIGN CALCULATION & PRESENTATION :
Abstract :Considering present day need to boost Ethanol production ,which enable Ethanol bleeding with Petrol. New policy of Govt of India allows Ethanol production from BH molasses ( 55% F.S),sugar cane juice,syrup & alternate feed stocks like Sugar Beet,cassava, rotten food grain etc.

## Slide 3
Further Govt of India revised the norms of BH & yield of Ethanol from BH & also revised the norms of Sugar cane syrup & yield of Ethanol from Syrup( 50% F.S).Rs 57.61 liters/ton of Ethanol produced fro BH( 55% F.S) &Rs 62.65 /liter in case of Ethanol produced from Syrup& Rs 45.69 in case of Ethanol from A grade Final molasses(50% TRS).We have chosen a Standard sugar plant of producing plantation white Sugar .Corresponding Evaporator requirement & configuration is worked out in both the cases & for comparision ,normal case without diversion is also considered.

## Slide 4
Methodolgy of Evaporator Calculations
1) Target 5000 TCD :With 2 massecuite boiling & BH diversion to Ethanol .The syrup goes for A&B boing.
2) Target 5000 TCD: Up to Evaporator station,& then syrup quantity corresponding to 1000 TCD is diverted to Ethanol making.Remaining syrup goes for2 massecuite boiling .
For comparision : Target 5000 TCD & then total syrup goes for three massecuite boiling .Then Final molasses (CH) goes to Ethanol making.

## Slide 6
OPERATIONAL DETAILS | SCHEME I | SCHEMEII
TCD/TCH | 4507.41/204.88 | 4507.41/204.88
Imbibition% fib | 202 | 202
Mixed juice %cane | 104 | 104
Load to Juice heaters % cane | 116 | 116
Clear juice % cane/Brix ( after DCH) | 107.32/13.73 | 107.32/13.73
Syrup Brix | 60 | 60
% Evaporation | 77.11 | 77.11

## Slide 7
Bleeding pattern | Scheme I | Scheme II
M.J 1st heating ( 32 -45 ⁰C) | V body out let vapours | Same
M.J 2nd heating ( 45 – 60 ⁰C) | By condensate cross heating | Same
M.J .correction heating ( 60 -70 ⁰ C) | By 4th vapours by Dynamic J.H | Same
S.J 1st heating ( 65 – 85 ⁰ C) | By 3rd body vapours | Same
S.J 2nd heating ( 85 -95 ⁰ C) | By 2nd Vapours | Same
S.J .Final heating ( 95 – 102 ⁰C) | By 1st Vapours by D.C.H. | Same
Load to clarifiers | 117.42 % on cane | Same
Cl.J 1st heating ( 95 – 100 ⁰ C) | By P.T.H By 2nd vapours | Same
Cl.J 2nd heating ( 100 -111 ⁰ C) | By 1st Vapours by D.C.H | Same
Cl .J load to Evaporatorts | 106.47 % on cane @ 13.83 Bx | Same
Pan bleeding pattern | CVP sets for massecuite boiling | Same
A/B /C % cane | A-24 & B -11 % on cane | A -24 & B -11 % on cane
Vapour consumption kgs/kg of Massecuite by 3rd vapours | For A 0.4125 kgs/kg massecuite & 0.35 kgs/kg massecuite for B | For A 0.4125 kgs/kg massecuite & 0.35 kgs/kg massecuite for B
1st body inlet exh,. Pr /Temp | 2.01 kg/cm2.a/120.65 deg C | Same
Last body vapours | 0.2 kgs/cm2.a/60 deg C | Same

## Slide 8
Details | Scheme I | Scheme II
Body vapour pressures |  | 
I/II/III/IV/V | 1.61/1.23/0.87/0.53/0.20 kgs/cm2.a | Same
Corresponding Temp. in ⁰ C | 120.65/113.53/105.72/96.04/82.74/60 | Same
Corresponding Evaporation Kgs/hr I/II/III/IV/V | 56798/50383/43386/10475/68155 | 53693/47794/41021/14505/10845
Exhaust requirement in 1st effect | 56798 in Kgs/hr | 54052 in Kgs/hr
Condensate flash advantage | 1.5 % on cane | 1.5 % on cane
Net requirement | 537825 kgs/hr | 50979 kgs/hr
Overall steam requirement including Miscellaneous demand & losses | 57823 kgs/hr 28.27 % on cane rounded off to 28.50 % on cane | 55077 kgs/hr 26.88 % on cane rounded off to 27 % on cane
In the season BH diversion for 158 | Days & Partial syrup diversion | 44 days to Distillery
Net steam consumption | {(158 x 28.5 ) + (44 x 26.50 )} 202 | = 28.06 % on cane

## Slide 9
Details | Scheme I | Scheme II
Temp/BPE/Te/∆T/Coeff .of Evaporation | I – 113.53 ⁰C/1.4 / 114.93/5.72/4.93 | I- 113.53 ⁰C/1.45/114.98/5.67/4.957
 | II – 105.72/0.55/106.27 /7.26 /3.898 | II – 105.72 /0.55/106.27/7.26/3.973
 | III – 96.04/2.50/97.49/8.23/2.53 | III – 95.5 /2.50/97.50/8.22/2.7605
 | IV – 82.74/3.75/86.49/9.55/1.53 | IV – 82.74/3.7/86.44/9.06/1.654
 | V- 60 /6.85/66.85/15.89/0.8186 | V- 60/7.02/67.02/15.48/0.81/0.81
H.S.A in m2 | I - 2200 m2 S.K/II -2200 FFE /III -2500 R/IV – 750 R/V -550 RM2 | I-2150 M2 S.K /II – 2150 FFE/III -2200 R /IV – 1050 R/V- 1050R
Floating body /stand by in m2 | One floating body of FFE 2400 m2 for I & II | One floating body of FFE2300m2 as floating for I &II
 | Stand by R of 2500 for III | Stand by R of 2200 for III
 | One floating of 750 m2 R for IV & V | One floating of 1050 m2 R for IV &V

## Slide 10
Similarly the Brixes of Intermediate Molasses AL :75,AH :80,BH 85.All massecuite boiling by VKT’s
Massecuite % cane A-24,B-11 . Ctushing rate 4507TCD /204.88
Vapour requirement for A – 0.4125 & B-35 vapours/kg of massecuite. 3rd effect vapours for Raw massecuite boiling 13.75 %
Pan washing 0.5 % on cane by 2nd vapours ,
Seed meltinf 1.0 % on cane by 1st vapours
,Molasses conditioning by 3rd vapours 0.5%.
Steam for drier 0.1% by 1st vapours ,
C/F washing by 1st vapours 0.2% on cane.
Total Evaporation in Quintuple 76.95 % on cane 167856 kgs/hr .
Syrup quantity 24.54 % on cane 50280 kgs/hr

## Slide 11
.
Syrup quantity50280 kgs/hr ( 24.54 %) @ 60 Brix
Corresponding evaporation in Quintuple : I -56798/II-50383/III -43386/IV -10475/V- 6815 KGS/hr (1.096% on cane)
Exh Requirement : 56798 kgs/hr ( 27.72 % on cane). Condensate flash recovery 1.5 % on cane .Net steam consumption 26.22 % on cane.
Miscellaneous 1 % on cane & High pr & low pr.losses ( 1.0 % on cane.Total Estimated steam consumption 28.27 ≈ 28.50 % on cane
Avg Brixes I-16.21 II -22.83 III -29.59 IV -42.38/V-56.28
H.S.A distribution 2200 S.K/2200 FFE/2500 R/550 R/400R=8200 M2.H.S.A/TCD 1.82 m2/TCD i.e 40.02 m2/TCD .The ratio is on higher side ,because one has to consider recirculation of Juice into consideration..Evaporation rates 25.82/22.90/17.35/13.97/12.40 kgs/m2/hr 2400 FFE as floating for I/II 2500 R STDBY for III & 750R As std by for IV & 550 R as std.by for V

## Slide 12
II)Target crushing rate 5000 TCD ,up to Evaporator & syrup quantity corresponding to 1000 TCD is diverted to Ethanol.
Upto Clear juice load to Evaporators remains same.
The amount syrup going to panfloor is corresponding to 3507 TCD.
Hearafterwards the procedure is similar to BH diversion.Hence the calculation is omitted.
Considering condensate flash advantage & miscellaneous losses & high & low pressure losses ,The total estimated steam % cane =55077 kgs/hr (26.88 % on cane ).
Average Brixes estimated I-16.11/II -22.15/III -32.95/IV- 44.79/V- 54.71
. HAS’s estimated 2150 FFE/2150 FFE/2200 R-III/1050 R-IV /1050 R a sV = 8600 M2 .Ratio H.SA/T.C.D =1.91 M2/TCD Or 41.97 m2/TCH. Evaporation rates :24.97/22.23/18.60/13.81/10.33 kgs/m2/hr
2300 FFE as floating for I.II , 2200 R stand by for III & 1050 R as stand by for IV & V.

## Slide 13: Net steam consumption
In the season of 158 days BH is diverted to Ethanol & 44 days syrup is diverted to Distillery.
Net steam consumption :
{ 158 x 28.50 +44 x 26.88 }/( 158 +44) = 28.15 % on cane ,rounded off to 28.50% on cane.
In normal case of no diversion ,the total steam consumption : 29.85 % on cane ,rounded off to 30 % on cane.

## Slide 14: Scheme III: Normal 3 massecuite boiling with no diversion
With same bleeding pattern, 3rd vapours for massecuite boiling,.with similar procedure of estimating evaporator loads,then leaving Brix & average Brix,then coefficient of heat transfer ,the estimated areas are : ( here three massecuite boiling is considered for full load.
I -2300 S.K II-2300 FFE /III ( 1800 +1700 )R /IV -400 R / V-400 R .
Total heating surface /TCD : 8900/4507 = 1.97 M2/TCD ,43.44 m2/TCH.Floating bodies 2500 FFE for I&II,1800 R for III& 400 R floating for IV &V.
Evaporation rates : I- 26.15/II -23.24/III-13.27/IV -13.97 /V-5.57 Kgs/cm2/hr .Steam consumption61160 Kgs/hr 29.85% / 30 % cane.

## Slide 15
This is combined configuration for case I & II. For both BH diversion as well as for partial syrup diversion..
Take a bit higher heating surface 2400 m2 FFE for I& FFE of 2200 as II&R of 2500 III. Similarly take heating surface of 950 m2 R for IV effect.& 800 M2 R as V effect to be used Evaporation rates in I :25.82/22.90/17.35/13.97/12.40 in II 24.97/22.23/18.65/13.81/10.33 Kgs/m2/hr
Evaporator configuration Scheme I&II

## Slide 16
EVAPORATOR CONFIGURATION I,II&III (near impossible case)
This is combined configuration for Schemes I , II.&III For both BH diversion as well as for partial syrup diversion, as well as no diversion .
If we want to avail all options in one single set up ,then use :
FFE of 2500 m2 each for I&II ,(1800+1700 )R for III, 1600/500 R for IV,& 500 x2 R for V.
Floating bodies one 2500 m2 FFE for I,II&III,1400 R for III &IV, 500 R for V
Operate conveniently as per requirement
Next page General arrangement of two popular designs with details of juice distribution is given -------.>>>>

## Slide 17: Cleaning Schedule in case of BH diversion
Sr.No | Details | Range in days
1) | FFE/ S.K | 30 +/- 5 Days/ 35+/-5days
2) | FFE | 25 +/-5 days
3) | R | 20+/-3 days
4) | R | 10 +/- 2days
5) | R | 8+/ - 2 days

## Slide 18: Retention time
 | Dewtails | Time in minutes
FFE/S.K | 2500 M2/2300 M2 | FFE 2.31/S.K.11
FFE | 2500 M2 | FFE 3.30
R | 1800+1700 M2 | R 18/+R 17 = 35 (total)
R | 400 M2 | 10
R Total time ( FFE’s +R’s) Total time ( S.K +FFE +R’s) | 400 M2 | 10 61.01 min 69.30 min

## Slide 19
FFE DRAWINGS OF TWO POPULAR DESIGNS

## Slide 20: Juice distribution simplified view

## Slide 21: Distribution arrangement another view

## Slide 22
AUTOMATION TO BE CONSIDERED FOR FFE :
VFD’s are to be provided for Cl.J feed pump & Recirculation pumps. Flow meters are to be provided for recirculation duty & out let syrup. Flow control has to be provided for recirculation pumps. Heating steam flow control & vapour stabilization system s have to be provided. Brix measurement of inlet juice & out let syrup have to be provided. Brix control to be provided for out going syrup. Condenser Automation to be considered.

## Slide 23: Role of Vertical Continuous pans
Various features:
*This is designed to work with low pr. Vapours
Five symmetrical calendria for massecuite boing & tightening.For better massecuie quality graining pan in separate batch pans .Stainless steel wetted parts.
*Top mounted mechanical circulator with VFD in all chambers.Compact mechanical seals.
Honeycomb calendria for improved circulation.Induces increased heat transfer coeffcients . Imroved performance because of Mechanical circulation & optimum downtake diameter of 37% of Clendria diameter. It also results in optimum tube height & level above top tubeplate & optimum vapour space heights.

## Slide 24
G.A OF CVP

## Slide 25: OVER VIEW OF HONEYCOMB CALENDRIA

## Slide 26
*Operating pressure upto 700 mbar for low massecuite & 600 mmbar for high massecuite boiling.
*Improved crystal yield ,reduced incrustation,& reduction in formation of conglamorates.
Inlet vapour control & for individual chambers .Massecuite level & temperature measurements.
* Efficient Automation of all variables.
* Cleaning during operation by isolating of individual chambers.
* Less load on condenser
* Vertical Installation & does not need supporting structure.

## Slide 27: CVP AUTOMATION TO BE CONSIDERED
The Automation include heating vapour control loop,hot water control loop,Brix control/indication loop,condensate measurement in the tightening zone. This is apart from regular automation being provided in the boiling zone of CVP ,which include Brix measurement & control for Alternate compartments ,heating vapour control,ratio control for Magma/molasses,absolute pr.control etc based on PLC system with SCADA ,which could be hooked to DCS of the plant automation.
The measurement of Molasses/Syrup & Condensate is considered. Level indication & control for feed molasses & level indication of seed magma crystallizer ,are essential

## Slide 28: PRECAUTIONS TO BE TAKEN
These measures are sensitive to fluctuations .
Ample Imbibition % fibre 250+to be provided for effective vapour bleeding. Similarly the Brixes of intermediate molasses: AL :75 ,AH -75,BH 83.5,CL-80
Systems governed by Automation needs steady state conditions.
For plants 5000 TCD &above need to run on minimum 70- 75% of rated capacity on TCD basis.
System of Automation needs qualified & Trained Instrumentation engineers & Techniciens .Regular Training programmes on the aspect of operation & maintenance to upgrade the skills ARE a must.

## Slide 29: Observation with remarks & conclusion: Considering the present day scenario with surplussugar production,the manufacture of Raw Sugar followed by Refined sugar & special emphasis on Ethanol production on the routes of BH diversion & partial syrup diversion is considered & based on Govt of India guidelines. We have chosen 5000 TCD PWSplant with above two routes & It is observed the Partial syrup diversion to Ethanol gives less steam consumption 26.50 % on cane ,followed by BH diversion 28.5 % & then maximum 30% with normal operation. Hense Partial syrup route in benefitial to the factories as far as steam consumption is concerned.

## Slide 30: THANKS FOR ANALYTICAL & PATIENT LISENING