## Slide 1
Technical Research Paper entitled ‘"In case of BH diversion / partial syrup diversion to Ethanol production -recovery calculations ,Ethanol yield data & related Ethanol economics. Improvement in sugar quality while diverting these feed stocks to Ethanol production”

## Slide 2
Authours name : Sura Kuppuswamy Bhojaraj
Specific method of Research:
Keeping in view of present day trend , to keep sugar production in control , two routes are selected:
BH diversion ( 2 massecuite boiling) to Ethanol production &
Partial syrup diversion ( 2 cmassecuite boiling ) to Ethanol production ,along with Final molasses .
The recovery calculation in each case is computed & compared with normal 3 massecuite boiling recovery.
In these cases ,in BH diversion resulting in two massecuite boiling , there is reduction in melt quantity ,affecting Sugar quality. We have taken up improvement of sugar quality aspect.

## Slide 3
RESEARCH DESIGN CALCULATION & PRESENTATION :
Abstract :Considering present day need to boost Ethanol production ,which enable Ethanol bleeding with Petrol. New policy of Govt of India allows Ethanol production from BH molasses ,sugar cane juice,syrup & alternate feed stocks like Sugar Beet,cassava, rotten food grain etc.Further Govt of India revised the norms of BH & yield of Ethanol from BH & also revised the norms of Sugar cane syrup & yield of Ethanol from Syrup.Rs 57.61 /liter of Ethanol produced from BH( 50% F.S) &Rs 62.65 /liter in case of Ethanol produced from Syrup( 55%F.S)& Rs 45.69 /liter in case of Ethanol from final molasses.
With above norms ,with BH ( 55% F.S),yield of Ethanol is 310 liters/ton .For Syrup with 50 % F.S ,the yield of Ethanol is 290 liters /ton .For A grade Final molasses with 50 % TRS ,the yield is 260 liters/ton.

## Slide 4
Introduction
Methodolgy of Evaporator Calculations
1) Target 5000 TCD :With 2 massecuite boiling & BH diversion to Ethanol .The syrup goes for A&B massecuite boing.
2) Target 5000 TCD: Up to Evaporator station,& then syrup quantity corresponding to 9.75 TCD is diverted to Ethanol making. Remaining syrup goes for 2 massecuite boiling ..
For massecuite boiling by 3rd vapours
Various standard steam economy measures are adopted.

## Slide 6: A)Recovery ,Ethanol yield data: Please refer annexure Ia ethanol economics in text
Nomenclature : A = Respective sugar quantity B-Syrup /molasses % cane x days of diversion ,
Total Ethanol production ,C= Estimated yield in liters/son , R1 =estimated overall recovery ,Ax B = Ethanol production during off season ,Basis : Season days of 202days are considered.
Basis:Total cane 5000 TCD /24 hours .Actual achireved rate 4507 Tons /day
Estimated yield litres/ton : In case of Syrup 290lits/ton @ 55% F.S ( rate Rs 62.65/litr. In case of BH (@ 50% F.S ,310 Liters/ton (rate Rs 57.61/lit).In case of A’ grade molasses 260 liters/ton @ 50% TRS (rate Rs 45.69/lit) .F.M production w/o syrup diversion @ 90 Brix /purity 42.81.
Further Syrup % cane multiplied by pol% will give sugar quantity in Syrup. This figure x 600 will give Ethanol yield.

## Slide 7: Estimated loss % with 4507 tons crush rate 1.89.Estimated recovery 8.697. Good quality sugar price Rs 33/kg
Explanation step by step :
1) Syrup diversion : Corresponding to 9.75 Tons/hr is considered.
Syrup quantity 9.75T/hr ( this is the actual quantity sent to Distillery.)
% on total cane crushed :(9.75 x24 x 44 days) 10296/910497.037 = 1.131. Syrup at 58.25 Bx is considered for divresion. Here we consider 58.25 Bx Corresponding Syrup quantity 9.75 x 24 x 44 = 10296 Tons/season
2) BH diversion : see next slide

## Slide 8
In the season BH diverted for 158 days out of 202 days to Distillery & the rest 0f 44 days syrup at thye rate 9.75 t/hr to the distillery . Balance BH is stored in a storage tank & sent to Distillery.
BH diversion for 158 days @ 15.73 T/hr ( 59648 tons/910497.037 tons of cane ) = 6.55 % on cane.
Estimated recovery in BH : Actual recovery + loss in BH = 8.697 + 3.148 = 11.845 rounded off to 11.85
Total loss in recovery in BH diversion = 11.845 - 8.697 = 3.148
Equivalent sugar bags loss in recovery = 3.148 x 910497.037 /10 = 28624.394 x 3300 /10000000 = 94.586 crores.
Estimated recovery in Syrup = 8.697 + 0.54 = 9.237
Total loss in recovery in Syrup diversion = 9.237 - 8.697 = 0.54
Equivalent sugar bags for loss in recovery = 0.54 x 910497.037 /10 = 49166.84 x 3300 =16.225 crores.

## Slide 9
Total Ethanol produced in liters during season ( 158 days)
i) Ethanol production in liters during season : BH quantity 59648 x yield in lits/ton 328 x 158 days x 59.08 rate/liter =
59648 x 328 x 158 / 202 = 15300394.61 x 59.08 /lit = 90.39 crores
ii) Ethanol produced in liters during off season : 59648 x 328 x 59/202 = 57134396.515 x rate 59.08 /liter = 33.755 crores
iii) Ethanol produced in season from Syrup = 4916.684 x 600 = 2950010 .4 x 63.08 /liter = 18.72 crores
Total Ethanol production in liters : 90.39 +33.755+ 18.72 = Rs 142 .865 crores.
Total loss in recovery in case of BH = 3.148 x 910497.037 /10 = 28624.394
Value in crores = 286624 x 3300 / 10000000 =94.586 crores
Revenue due to sugar produced in crores = 910497.037 x 8.697 x 3300/10/10000000 x 158 /202 = 204 crores ( BH diverted in 158 days)

## Slide 11
Revenue due to sugar produced when Syrup is diverted for 44 days in the season
910497.037 x 8.697 x (3300/10 ) /10000000} 44/202 = 57.48 & taken as 57 crores
Revenue in crores : 204 ( sugar in season ) +90.39 ( Ethanol in the season)+33.755 ( Ethanol in the off season )= 328.15 crores
Real gain in crores = 328 .15 – Sugar lost to BH ( 94.586 ) = Rs 233.564 crores in case of BH diversion
In case of Syrup diversion : 57 + 18.72 = 75.72crors
Gross revenue = 75.72 -16.225 = 59.495 crores

## Slide 14
Overall view diversion of BH & partial syrup is 233.564+59.495 = 293.059 crore
In comparison ,if there are no diversions & only normal production & production of Ethanol from CH molasses.
FRP recovery as per guide lines : Recovery of 11.081 ,the production of normal sugar at estimated crushing rate of 910497.037ons for season ( 202 days):
910497.037 x 11.081 = 100892.1767 quintals
100892.1767 x 3300 ( Rs 3300/quintal ) ; Rs 332.944 crores

## Slide 15
Next FM production rate of 5.02 % ( yield of 260 lit/ton of ethanol at the rate of Rs 45.69/lit of Ethanol )
910497.037 x 0.0502 x 260 x 45.69 = Rs 54.300 crores.
Total Sugar +Ethanol from final molasses = 332.944 + 54.30 = Rs 387.244 crores.
Component wise Sugar comes down by (Rs 332.944 – 148.189) = Rs 184.755 crores ( 55%).
Ethanol goes up from 54.30 crores to 142.865 crores by 88.565 crores ( 163 %)
Over all sugar + Ethanol :Rs/ 291.059 crores when compared to Rs 387.244 comes down by Rs 96.185crores. Loss of 33%

## Slide 16
B)*As per govt of India guide lines BH & CH cannot be produced simultaneously.
The quantity of BH molasses produces is more than final molasses ( 6.55 vs 5.02 in this case). The sizing of Distillery also varies . Due to these reasons Sugar mills have to look for excess storage of molasses. To maintain keeping quality of molasses,it is to be cooled up to 40 + deg C .For this additional cooling facility is to be provided.
Losses in storage :
Obviously causes of molasses deterioration are to be kept in mind :
> Microbial growth , Milard reaction due to rise in temp .

## Slide 17
Low vapour consumption results in more load on condensers ,may result in low syrup Brixes.
In case of BH , resulting in two massecuite boiling , hence there will be reduction of 7.5 -8.5 % in total massecuite.
For this shifting the juice bleeding pattern & third body bleeding for pans to be practiced. Other way is to convert Evaporator configuration from Quintuple to Quad. A compramise in steam economy to be made.
Increase in sugar colour due to reduction in A massecuite purity .
In case of BH diversion ( two massecuite boiling ),obviously there is no C sugar melt ,hence A massecuite colour increases by 2- 3 % ,which results in slightly higher sugar colour up to 4 %

## Slide 18
Change in Pan boiling scheme :
Use of A1 massecuite boiling by using syrup & AH molasses. In this A1 massecuite purity can be maintained in the range 80 -81 & A1H will be produced of 63-64 purity. A1 sugar purity must be above 98, which could be utilized to increase to increase A massecuite purity & lower the massecuite colour , ultimately lowering the product sugar colour.
Use of A2 massecuite boiling by using AL ( above 85 purity )& AH purity near about 76 . The intermediate A2 massecuite is produced from low purity AL molasses. In this boiling scheme A2 massecuite purity could be maintained in the range of 83-84 & A2H will be in the range of 63-64 purity . A2 sugar purity must be above 98, which could be utilized to increase to increase A massecuite purity & lower the massecuite colour , ultimately lowering the product sugar colour.
Colour precipitant may be required to be used.

## Slide 19
Double curing of B massecuite :
. The Brix of BH molasses need to be maintained above 85 for better keeping quality of molasses.For maintaining this Brix low lubrication water to be applied at the time of curing B massecuite,by giving high colour to B seed & obviously colour of sugar will increase.To maintain desired Brix of BH molasses & colour of B seed for getting good quality of sugar it is preferred to follow B massecuite double curing
The colour of BFW sugar should be in the range of 3000 -3500 IU, in 2nd curing we could improve BAW sugar colour in the range of 1000 – 1200 IU. For this CAW continuous machine which is idle could be utilized & BAW sugar purity shall be always maintained above 96.
Need of B1 & B2 massecuite boiling :
The Raw juice purity in the states of Maharashtra,Karnataka ,Gujarat & M.P, in the latter part of crushing season touches above 85 .Then

## Slide 20
A massecuite purity reaches 90+.Due to low RS/100 Brix in juice below 3.5,purity drop in A massecuite is limited to 12-13& in this case AH purity remains in the range of 77-78 .In this situation it is not possible to control BH purity of the order 52-54. On the other hand ,there is enough vapour availabilty of pan & centrifugal capacity. In this situation allows us to follow B1 & B2 massecuite boiling & achieve advantages such as controlled BH purity,good utilization of vapour & pan capacity to achieve good sugar quality. The following steps to follow:
Follow common grain for B1& B2
B1 & B2 massecuite ratio : 1:2
B1 massecuite is to be boiled with AH & B1H molasses used for B2 massecuite boiling –topping
Separate cooling of B1 & B2 massecuites
B1 & B2 massecuite % cane 14-15

## Slide 21
* Increase in massecuite % cane 2-3.0
Advantages :
Good control over BH Brix & purity
B1 sugar lower < 1500 IU – better for A footing.
Good melt availability for A massecuite to reduce A massecuite colour – in the range 8000 -9000 partcularly in Maharashtra & Karnataka
Good sugar quality.
Precautions to be taken :
The syrup up to 60 Brix need to be cooled on line & taken directly to fermentation . This is through horizontal shell & tube syrup cooler .
If required an insulated buffer tank of about 2 hours retention time could be added before cooling the syrup. Concentrated syrup is a rich fermentation media & susceptible for contamination. Hence sufficient care has to be taken at all stages

## Slide 22
OBSERVATIONS & REMARKS
It is a special case of BH diversion for major part of the season 78 % & partial syrup diversion in the later part 22%. The balance BHY produced is stored in a storage tank & during off season sent to Distillery. In both cases 2 massecuite boiling is considered.
. In both cases production of normal white sugar is practised. The results are compared with normal three massecuite boiling w/o diversion.In comparision diversion is benefitial in case of Ethanol production About 34% more product value than normal white sugar production. The sugar production comes down by 55% at the same time Ethanol production increases by 163 %

## Slide 23
This presentation is limited to diversion characteristics ,hence process chemical costs & packing costs are not considered. This project is in implementation stage & will be coming out with all the details needed after completion of project during next season.
Similarly FRP recovery is calculated on the basis of Final molasses purity of 36.40 as per Govt.agencies such as N.S.I,V.S.I & Federation of Coperative sugar factories etc. We are going as per factory data ,as of now.
Acknowledgement : The authour is grateful to both SISSTA governing council & management of Sri Nijalingappa sugar institute ,for giving necessary encouragement & permission to publish this article.Author also puts in record ,the timely information & guidance given by DSTA colleagues Prof .B.B.Gunjal , Mr.V.M.Kulkarni & Prof. K.Jagdish. Also special thanks to Mr.C.Ramamohan ,Production Manager of Sadguru Sri Sri Sugar Factory near Pandharpur , who has helped me in making the recovery calculations & Computer evaluation

## Slide 24: Thanks for analytical & patient listening

## Slide 30: :

## Slide 32: THANKS FOR ANALYTICAL & PATIENT LISENING